## Slide 1
Vehicle readout analysis
Decode a VIN readout, see what it means, check software versions and baselines
What the tool contains and how to add features
FaultTracing-Scripts · decoder/
Notes: Introduce the tool: one Streamlit app that takes a VIN, loads its readouts, translates them with an SDDB, explains them, and shows software versions. The second half shows how colleagues can extend it.

## Slide 2
Why this tool
Vehicle readout analysis · FaultTracing-Scripts
2
The problem
• A readout is raw UDS hex, per ECU and per DID
• Meaning needs the SDDB and platform knowledge: HPA is controlled by HIA, LPA keeps standby history
• Software versions are in ConfigHub
• HIA and HIB reset logs needed an Excel macro
The tool
• Enter a VIN and load its readouts from the share
• Translate them with the right SDDB
• Read rule-based findings and recorded tables
• See software part numbers and MAIN_INT baselines, with links
Notes: A readout is a pile of UDS responses. Reading it needs the SDDB, knowledge of how HPA, HIA, HIB and LPA relate, and separate tools for versions and reset logs. The app puts these in one place.

## Slide 3
How it works
Vehicle readout analysis · FaultTracing-Scripts
3
VIN
enter a VIN or pick a file
Readout share
SMB; readouts found in parallel
SDDB
ECUs, DIDs, DTCs; indexed once, cached
Translated readout
decoded text per ECU and DID
Translated readout tab
ECU tree, search, lookup, download
Readout summary tab
interpretation rules, timeline, recorded tables, reset logs
SW versions tab
part numbers, ConfigHub baselines, file links
Everything slow is cached: SDDB index about 25 s once, then about 2 s; readout discovery 80 s down to 6 s
Sections, trees and expanders start collapsed; tables word-wrap
A fourth tab, Compare readouts, lists what changed between two readouts of the same VIN, node by node
Notes: Left to right: VIN to readout files on the share, the SDDB gives names to ECUs, DIDs and DTCs, the translated readout feeds three tabs.

## Slide 4
Tab 1: Translated readout
Vehicle readout analysis · FaultTracing-Scripts
4
ECU tree ECU, then its readouts; collapsed until you open it, tick what to show
Search and filter decoded text, ECU, DID or DTC
Lookup by ECU, service or DID
Output terminal-style, with the matches highlighted
Download the full translated readout as a text file
Source VIN on the share (latest readouts first), or an uploaded or chosen file; SDDB from a file browser
Notes: Show the ECU tree, tick a readout to see it in the output pane, search the decoded text, filter by ECU or DID.

## Slide 5
Tab 2: Readout summary
Vehicle readout analysis · FaultTracing-Scripts
5
Interpretation
• Findings: issue, warning, info, ok, with counts
• Each opens to its evidence and source readouts
• Timeline merges standby cycles, FSI errors, platform states, DTCs and HIA restarts
• HIA and HIB reset logs (22 FE 04): common data, reset history, application context
• Application watchdog table with Essential and Restartable columns
Recorded data (standby decoder)
• Standby events of HPA
• FE03 error slots and reference details
• Platform state transitions
• ECU DTC snapshots with UTC time
• Watchdog information
All sections are collapsed and open on click.
The whole summary downloads as one Markdown report: every finding with its tables, the timeline, all recorded tables and the raw output.
Notes: Interpretation first: findings are sorted by severity and open on click to show the evidence and which readouts to check. Below are the standby decoder's recorded tables.

## Slide 6
The platform model behind the findings
Vehicle readout analysis · FaultTracing-Scripts
6
HPA
High Performance, QNX. Sleep or standby (SC7); essential applications
HIA
High Integrity A. Controls HPA, stores HPA reset reasons and standby failures
HIB
High Integrity B. Resets on its own, keeps a reset log
FSI error
reset / cold boot
LPA
Standby history of SGA, HPA, HIA, HIB
Standby fails reasons are stored in HIA and HPA cold boots instead of resuming
Essential application over its restart limit HIA resets HPA
A failure or reset of HIA can restart HPA
An HPA standby failure does not show in LPA HIA powers off anyway, so LPA counts matter for the other nodes
Notes: These are the domain statements the rules encode. They are the source of truth: a rule must not contradict them.

## Slide 7
Example: what one real readout told us
Vehicle readout analysis · FaultTracing-Scripts
7
HIA restarted HP on 2026-10-07: cold boot, with thermal and power reasons recorded
HPA standby failures 3 counted by HIA (LPA shows none, as the model predicts)
FSI errors 19 error slots recorded and classified by origin
Application watchdog 150 non-essential application failures, none essential abandoned
HIB reset log last reset ERROR_HOOK, exceptional, reset counter 6, with a stack trace
LPA clean history for the other nodes
Each finding lists its source readouts, for example HIA 22 FE 14, so you can check it in tab 1.
Notes: Abbreviated from a real readout of 2026-10-16. The point is the kind of statement the tool produces, with evidence one click away.

## Slide 8
Tab 3: SW versions
Vehicle readout analysis · FaultTracing-Scripts
8
Part numbers
• HIA, HIB, HPA, SGA, VESA, VESB
• Software modules with part number and edition, for example 32489651 ACP
• Diagnostic database, calibration, fingerprint
• Core, delivery and serial numbers shown once when all ECUs agree
MAIN_INT baselines (ConfigHub)
• One matching call per ECU, in parallel: about 6 to 11 s
• HPA is two ConfigHub positions: HPA and HPAA
• Links to each baseline in ConfigHub
• Download column: each part's .vbf; your browser signs in to Artifactory
• Certificates and 00000000 placeholders are ignored
• ConfigHub returns its best three matches, so only the newest versions show
Notes: Part numbers come from the identification DIDs of each ECU. The baseline lookup is optional and needs ConfigHub access.

## Slide 9
Where things live
Vehicle readout analysis · FaultTracing-Scripts
9
decoder/decoder.py
Streamlit UI: tabs, ECU tree, tables, buttons
decoder/streamlit_workflow.py
Readout discovery on the share, SDDB index, translation cache, summary parser
decoder/interpretation.py
Rules, severities, timeline
decoder/reset_log.py
HIA and HIB reset log decoder (port of the Excel macro)
decoder/summary_report.py
Markdown report of the Readout summary tab
decoder/sw_versions.py
Part numbers from the identification DIDs
decoder/baselines.py
ConfigHub baseline matching and links (uses confighub_lookup.py)
decoder/test_decoder.py
Unit tests for the decoder app
Submodules SAT_Readout_decoder (translates readouts with an SDDB) and standby-decoder (summary tables)
Skill .github/skills/decoder-summary-interpretation holds the platform model, the DID map and the rule catalog
Notes: The UI is decoder.py. Everything that decides or fetches is in its own module, so a new feature usually touches one module plus a few lines in decoder.py.

## Slide 10
Run it
Vehicle readout analysis · FaultTracing-Scripts
10
VPN the readout share and ConfigHub
SDDB file put it in ~/Downloads/sddb, or set SAT_SDDB_DIR
ConfigHub login saved in the OS keychain by confighub_lookup.py, or typed into the app
Share login optional; saved in the keychain from the app
git clone git@github.com:vkumar-vcc/
FaultTracing-Scripts.git
cd FaultTracing-Scripts
.\setup_uv.ps1
.\.venv\Scripts\Activate.ps1
uv run streamlit run decoder\decoder.py
Then: enter a VIN, Load readouts, choose the SDDB, Translate.
Notes: You need VPN for the readout share and ConfigHub, and an SDDB file for the vehicle platform.

## Slide 11
Add a feature 1: a new interpretation rule
Vehicle readout analysis · FaultTracing-Scripts
11
State the claim and tie it to a platform statement
Find the DID in readout-data-map.md; decode a real readout if missing
Write the rule rule_<topic>(context) in interpretation.py; return [] when data is absent
Pick a severity issue, warning, info or ok
Show the evidence evidence or table, plus sources
Validate on a real readout; add it to rule-catalog.md
def rule_example(context):
values = context.values("HIA", "22FE14")
if not values:
return []
failures = to_int(values.get(
"HPA Standby Transition Failure Counter"))
if not failures:
return []
return [finding(
"HPA standby and resume", "issue",
f"HIA counted {failures} failed HPA "
"standby transition(s)",
sources=["HIA 22 FE 14"])]
RULES.append(rule_example)
Notes: This is the most common extension. A rule is a function that reads the translated readout and returns findings. The skill file documents the same steps.

## Slide 12
Add a feature 2: a new decoder, or a new section
Vehicle readout analysis · FaultTracing-Scripts
12
A new DID decoder
• Own module, no Streamlit: bytes in, rows out (reset_log.py)
• Take the layout from the source of truth and check it against real data
• Return it from a rule: finding(table=..., extra_tables=[(title, headers, rows)])
• Say in the finding text what is assumed
• Add the DID and layout to readout-data-map.md
A new section or tab
• Write render_<name>(result) in decoder.py and add it to st.tabs(...)
• Keep results in the result dict; run slow calls in worker threads (baselines.py)
• Use render_wrapped_table; a cell can be a list of (text, url) links
• Expanders and sections start collapsed
• Cache outside calls, as baselines.py does for an hour
Notes: reset_log.py is the model for a new decoder: pure Python, bytes in and rows out. baselines.py is the model for a section that calls an outside service.

## Slide 13
Ground rules for changes
Vehicle readout analysis · FaultTracing-Scripts
13
Do not invent data show what the readout says; mark every assumption in the output
Validate on a real readout a synthetic example is not enough
Hedge conclusions "indicates", "consistent with"; show the evidence and source readouts
Never break the page for missing data a rule without its data returns nothing
Keep it fast cache heavy work, use threads for network calls
Update the docs in the same change rule catalog, data map, README
Never print or store secrets logins go to the OS keychain
Notes: These keep the tool trustworthy. The interpretation findings are read by people deciding what to fix.

## Slide 14
Use the skill when you extend it
Vehicle readout analysis · FaultTracing-Scripts
14
.github/skills/decoder-summary-interpretation/ the folder
SKILL.md platform statements, how to add or change a rule, severity meanings
references/knowledge-model.md the model in detail and the open questions
references/readout-data-map.md DIDs by ECU, fields, reset log layout, ConfigHub calls
references/rule-catalog.md every rule, its inputs and severities, and the finding shape
Ask Copilot, for example: "add a rule that flags HIB resets by ERROR_HOOK". The skill gives it the platform model and the steps.
Notes: The skill is a folder of markdown files that Copilot loads on request, and that a person can read as documentation.

## Slide 15
Known limits and ideas
Vehicle readout analysis · FaultTracing-Scripts
15
Known limits
• Baselines: ConfigHub returns its best three matches, so only the newest versions show
• A part number tells which baselines contain it, not which one was installed
• Reset log: structure version 0002 differs from the 0001.0002 the Excel sheet was written for; the application context decoding is unverified
• The application context decoding is chosen from the reset reason (an assumption)
• Part file downloads need an Artifactory login in the browser
Ideas
• Compare readouts of different VINs
• More rules, starting with the open questions in knowledge-model.md
• Reset log from UART text, as the Excel sheet allows
• Rules for SGA and the VES nodes
Notes: Limits are what to keep in mind when reading results. Ideas are suggestions, not commitments.

## Slide 16
Where to find it
Vehicle readout analysis · FaultTracing-Scripts
16
Repository github.com/vkumar-vcc/FaultTracing-Scripts
App decoder/decoder.py, started with uv run streamlit run decoder\decoder.py
Docs README.md, section "Combined Streamlit app"
Skill .github/skills/decoder-summary-interpretation/
Tests decoder/test_decoder.py
Questions, or a rule you want added? Open an issue or send a pull request.